Single Stage LNA - Objectives
Design of a low noise amplifier with noise figure target of less than 0.4 dB
Implementation within antenna feed to avoid any cable, adapter or connector between antenna and LNA
All additional passive components in front of the first amplifier stage will increase noise figure according to their insertion loss
Small design required -> single stage for integration inside antenna
Design on RF PCB material RO4003 due to less loss (tan δ = 0.0027) versus FR4 (tan δ = 0.0027)
Avago transistor ATF34143 chosen because of its typical noise parameter (Fmin = 0.14 dB @ 1.5 GHz, UDS = 3 V, ID = ´20 mA)
Negativ gate biasing voltage required, ICL7660 used to supply negative voltage

---
Single Stage LNA - Objectives
Self-biasing transistor stage with disadvantage of worse input reflection S11
Source transmission lines used to deal with S11 versus input noise matching
S11 target < 8 dB
Source transmission lines improve Rollet stability factor at low frequencies (<5 GHz)
Low pass matching filters and drain resistor required for better stability
Rollet factor target < 1 for unconditional stability
Unconditional stability required because of unknown load impedance/ unknown bandpass filter design

---
Single Stage LNA - Schematic

---
Single Stage LNA - Components

---
Single Stage LNA – Layout on RO4003

---
Measured input and output matching

---
Measured Gain and stability factor

---
Measured noise figure 0.7 dB :-(